## Slide 1
Lab Book 2.0. Couplers
Student: David Alcarria Pedro

## Slide 2: Instructions General
SCRIPTS
From GitHub 
  Fork the repo: https://github.com/cccanvas-upv/pic-upv-lab2.git
  Clone the repo using VSCode
Run the Jupyter Notebook:
  COUPLERS_Student.ipynb
Cross-Sections to be studied:
h
(height)
w (width)
Core
Cladding
w (width)
MMI Body
Cladding
Multimode Interference (MMI) coupler
Directional coupler (DC)
Core
g
(gap)
h
(height)

## Slide 3
Directional coupler

## Slide 4: Learning outcome #1 – Directional coupler length and coupling coefficient Wavelength 1.5 µm – width 1.2 µm – gap 0.6 µm
Comment results (distance needed for a complete energy transfer between waveguides, distance needed for splitting power in half.. )
Cuando L=m*L_pi siendo m valores enteros positivos impares por 1 obtenemos una transferencia total de energía entre guías ya que K=1.
Para obtener la potencia dividida entre los dos puertos de salida L = m*L_pi/2 para valores de m impares.
Por ultimo, para tener K=0 hemos de poner una distancia L=m*L_pi para m pares.
deep waveguide
Paste L/Lpi vs K plot here

## Slide 5: Learning outcome #2 – 2x2 Directional Coupler Gap 0.6 - 1.6 µm (step 0.1 µm) – Wavelength 1.55 µm
En el caso de la izquierda L=L_pi por tanto se obtiene la mayor parte de la potencia en la salida contraria al puerto de entrada como se puede observar en los ratios de salida.
En el caso de la derecha L=L_pi/2 por tanto la potencia de entrada se divide a la mitad en cada puerto de salida. Como se aprecia en la imagen, los ratios de salida son 0.5 en el puerto de arriba y 0.5 en el de abajo.
Ambos casos presentan una pérdidas de 0.18 dB.

## Slide 6: Learning outcome #2 – 2x2 Directional Coupler Gap 0.6 - 1.6 µm (step 0.1 µm) – Wavelength 1.55 µm
GAP (um) | LOSSES (dB) | L_pi RATIO
0,6 | 0.1851 | 0.9987
0,7 | 0.1161 | 0.9989
0,8 | 0.0968 | 0.9990
0,9 | 0.1191 | 0.9992
1 | 0.1938 | 0.9994
1,1 | 0.3345 | 0.9995
1,2 | 0.5452 | 0.9996
1,3 | 0.7669 | 0.9997
1,4 | 1.0870 | 0.9997
1,5 | 1.4155 | 0.9997
1,6 | 1.7769 | 0.9999

## Slide 7: Learning outcome #2 – 2x2 Directional Coupler Gap 0.6 - 1.6 µm (step 0.1 µm) – Wavelength 1.55 µm
Estas gráficas muestran la dependencia de las pérdidas y el ratio en los puertos de salida para cada valos del gap. Los mejores valores de gap estarán entre [0.7,0.9] ya que presentan las pérdidas más bajas y a su vez un ratio de salida bastante cercano a 1 que es el caso ideal.

## Slide 8: Learning outcome #3 – Parallel uncoupled waveguides Wavelength 1.55 µm, width 1.0 µm, gap to be found for uncoupled wvgs
Para que las guías estén desacopladas, Lπ debe ser mayor que L para minimizar K. Se podrían escoger valores de gap relativamente pequeños que cumplan la condición, pero como K es oscilatorio, en algunos puntos puede acercarse a 0 de manera accidental; sin embargo, las guías no estarán realmente desacopladas.
Para el caso deep obtenemos un gap de 3.6 um y cumple con que el Lpi correspondiente (183.91 mm) es mucho mayor que L.
Para el shallow, he cambiado la función eme.py porque no calculaba para casos shallow
deep waveguide
Paste vs gap for 10 mm wvgs to be uncoupled
shallow waveguide
Paste vs gap for 10 mm wvgs to be uncoupled

## Slide 9
Multimode Interferometer (MMI) Coupler

## Slide 10: Learning outcome #4 – 4.1 2x2 Multimode Interference Coupler Wavelength 1.55 µm, wMMI = 6.6 µm
Comment results (Coupling relationship, Lpi, losses, comparison with Directional Coupler… )
Para el caso de Lpi/2, obtenemos unas pérdidas de 0.4217 dB y un ratio de salida cercano al 50/50 esperado (0.5152 y 0.4848)

## Slide 11: Learning outcome #4.2 – 2x2 Multimode Interference Coupler - Optimization Wavelength 1.55 µm, wMMI = 6.6 µm
Comment results
Con valores de dy = 0.1 y de dL_MMI = -0.5 obtenemos unas pérdidas optimizadas de 0.330 dB y un ratio de 0.5055 y 0.4945
Target: make equal ratio over outputs (even if not 0.5) and minimize excess loss (even if not 0.0 dB)
With same settings of previous LO, now adjust try to manually optimize the MMI by changing iteratively:
- Change dL_MMI
- Change I/O waveguide position +/- dy
Hints: observe the 2D EME propagation results to guide you to the best settings of a) and b).

## Slide 12: Learning outcome #4.3 – 2x2 Multimode Interference Coupler – Optimization (II) Wavelength 1.55 µm, wMMI = 6.6 µm
Comment results
Para un width de 1.3 um obtenemos muy buenas pérdidas (0.0159 dB) aunque no llegue a bajar de los 0.1 dB y unos ratios no tan cercanos al 50/50.
deep waveguide
Paste propagation plot and console results
Target: make ratio over outputs 0.5 + excess loss < 0.1 dB
With same settings of previous LO, now modify the notebook so I/O waveguides have a different width.
- The nominal I/O waveguide width you have been using is 1.0 µm, increase it.
(Warning! Every time you change the I/O waveguide width you have to re-run modes calculation)
Hints: observe the 2D EME propagation results to guide you to the best settings of a) and b).

## Slide 13: Learning outcome #5 – 1x4 Multimode Interference Coupler Wavelength 1.55 µm, wMMI = ? µm
Width = 12 um. Primera imagen sin optimizer y para 3*Lpi/16. Para la segunda gráfica hemos realizado la primera optimización con dy = 0.1 y dL = -1.2. Para este caso mejoramos las pérdidas pero los ratios son peores. Después de la segunda optimización con un width de 2 um, obtenemos unas muy buenas pérdidas (0.0015 dB) pero no tan buenos ratios de salidas.

## Slide 14: Extra #1 – Directional wavelength dependence Wavelengths from 1.5 to 1.7 µm, gap = 0.6 µm, width 1.0 µm
Comment results
slab = 150nm

## Slide 15: Extra #2 – Directional coupler gap dependence Wavelength 1.55 µm, width 1.0 µm, gap 0.2-2.4 µm (step 0.2 µm)
Make conclusions and observations from your results
slab = 150nm

## Slide 16: Extra #3 – MMI coupler wavelength dependence Wavelengths from 1.5 to 1.7 µm, wMMI = 6.6 µm
Comment results (Important. Compare with Directional Coupler)
slab = 150nm

## Slide 17: Extra #4 – MMI coupler body width dependence Wavelength 1.55 µm, wMMI = 5-10 µm (steps 0.5 µm)
Polarization independent coupler: is there any point for which the MMI coupler can work identically for TE and TM? Answer yes / no and explain why?
slab = 150nm

## Slide 18: Thank you